# SECTION 12 24 13

ROLLER WINDOW SHADES

GENERAL

  - SUMMARY

    - - Section Includes:

      - Manual roller shades.

      - Shade accessories.

  - REFERENCES

    - National Fire Protection Association (NFPA) (www.nfpa.org) 701 (2004) - Standard Methods of Fire Tests for Flame Propagation.

  - SYSTEM DESCRIPTION

    - Manual Roller Shades: The clutch shall be made of high-strength fiberglass reinforced polyester with high carbon steel springs.  And, shades shall stop upon release of clutch.

  - SUBMITTALS

    - Submittals for Review:

      - Shop Drawings; include:

        - Shade schedule indicating room number, opening sizes, quantities and key to details.

        - Head, jamb and sill details, and mounting dimension requirements for each product and mounting condition.

      - Samples:

        - Fabric sample showing specified color.

      - Product Data; include:

        - Descriptive literature and details for each product type including materials, finishes, construction, and dimensions of individual components, profiles, and mounting requirements.

    - Quality Control Submittals:

      - Test Reports: Indicating compliance with specified fabric properties.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications:

      - Assign responsibility for design, engineering, installation, and performance of window shade system to single manufacturer and their qualified dealers and installers.

      - Furnish shading system

      - Qualified to supply specified products and to honor claims against product presented in accordance with warranty.

    - Installer Qualifications: Qualified to install and commission specified products by prior factory training, minimum 3 years shades installation experience, demonstrated performance, and acceptance of any requirement of the manufacturer, subsidiary of the manufacturer, or licensed agent.

  - DELIVERY, STORAGE, AND HANDLING

    - Store products in manufacturer's unopened packaging until ready for installation.

    - Do not deliver shades until concrete, masonry, plaster, painting, and other wet work is complete and dry.

    - Deliver shades to project in protective packaging, labeled to identify each shade for each opening.

    - Include installation and maintenance instructions.

  - PROJECT CONDITIONS

    - Maintain environmental conditions in installation areas within manufacturer’s recommended limits:

      - Ambient operating temperature: 32 to 104 degrees F.

      - Humidity: 0 to 90 percent, non-condensing

    - Do not install products under environmental conditions outside manufacturer's absolute limits.

    - Do not install shade system until building is operating at ambient temperature and humidity ranges that are consistent with those intended for buildings ultimate use.

  - COORDINATION

    - Fabricate shades after obtaining field dimensions for each opening.

    - Coordinate construction of surrounding conditions to allow for timely field dimension verification.

  - WARRANTY

    - Provide manufacturer’s 5 years (at 100%) and an additional 3 years (50%) parts warranty for defective equipment on shades.

  - MAINTENANCE

    - Make ordering of new equipment for expansions, replacements, and spare parts available to qualified dealer or installer.

- - PRODUCTS

  - MANUFACTURERS

    - Contract Documents are based on manual roller shade systems by Lutron Electronics Co., Inc.; 7200 Suter Road, Coopersburg, PA 18036-1299 Telephone (800) 523-9466, http://www.lutron.com.  For project details, please contact Brenda Golwitzer at 515-554-4331 or bgolwitzer@int-sales.com.

    - Or, comparable, approved product by one of the following:

      - WT Shade/Windowtex

  - SYSTEM REQUIREMENTS

    - Manual Roller Shades System Description

          - Clutch Roller Shades shall be a ball chain-operated system utilizing a bidirectional wrap spring clutch and never require any adjustment of the shade.

          - The system must be capable of smoothly raising and lowering the shade to any desired height and maintaining that position without slippage.

          - The shade cannot be operable by any other means other than the chain. Pulling on the hem bar will not disengage the clutch.

          - The system will provide a maximum fabric gap of 0.75” per side.

          - Shade shall stop upon release of clutch.  Systems that slide to a stop are not acceptable.

          - Clutch may be mounted on either the right or left end of the roller tube and fabric may be forward or reverse rolled.

          - The clutch shall be made of high-strength fiberglass reinforced polyester with high carbon steel springs.

          - Manufacturer shall identify appropriate shade tube and clutch size based on shade size, fabric type, and application requirements.

          - Fabric shall be connected to tube with double-sided adhesive strip applied for exact and firm mounting of the fabric and for easy adjustment of fabric to prevent telescoping.

- A minimum of one turn of fabric will be placed on the roller before the working section of fabric starts to protect the fabric and smooth out the starting seam.

          - Chain will be made of #10 stainless steel 90-pound test ball chain. Chain will be provided with connector and upper and lower ball stops.

          - Clutch Idle End Cap: Two-piece unit consisting of an outside sleeve and center bearing shaft made of high-strength fiberglass reinforced polyester.

            - The outside sleeve shall be free to rotate on the shaft, providing the bearing surfaces on which the roller rides in order to provide a smooth and quiet rotation without wearing on the system.

          - Clutch Mounting Brackets

            - Shall be .072" galvanized steel

            - Shall be applicable for mounting inside, outside or to the ceiling, with the clutch on either the right or left side of the roller.

            - The clutch mounts flush to the face of the bracket resulting in the smallest possible light gap between fabric and window frame.

  - ROLLER SHADES

    - Mounting:

      - Brackets to provide symmetrical light gaps of 0.75 inch on each side of shade.

      - Roller shade leveling adjustment allowing leveling adjustment while roller shades are mounted to brackets.

      - Allow side-to-side adjustment up to 0.375 inch on each side while shade is mounted to bracket.

      - Projection adjustment up to 0.50 inch.

    - Shade Tube: Fabric connected to tube using double-sided adhesive strip with minimum of one turn of fabric on roller before working section of fabric starts.

    - Housing: (Specify which housing option) metal fascia with top back cover OR metal pocket with flap/hanger; color from manufacturer’s range of standard colors.

    - Fabric:

      - Fabric selection: 
Lutron: (Specify which fabric: Basketweave 90, Basketweave E-Screen or Basketweave 4000 Eco) in ( ) % openness; color: TBD

    - Bottom Bar: Lutron Designer hembar.

  - SOURCE QUALITY CONTROL

    - Perform full-function testing on completed assemblies prior to shipment.

- - EXECUTION

  - INSTALLATION

    - Install in accordance with manufacturer's instructions and approved Shop Drawings.

    - Install shades to provide smooth operation.

  - ADJUSTING

    - Adjust level, projection, and shade centering from mounting brackets.

    - Adjust fabric on tube if visibly telescoping.

  - DEMONSTRATION

    - Demonstrate proper operation and maintenance of window shade system to Owner.

  - SCHEDULEA

# END OF SECTION